## Slide 1
Call & Self-Stop System
Andon Implementation for Production Excellence
Building Quality at the Source Through Jidoka Principles
David E. Jones
30 Years Manufacturing Leadership | 17 Years Toyota Motor Corporation

## Slide 2
What is Call & Self-Stop?
CALL (Andon)
Visual signal system using lights and boards to indicate production status. • GREEN = Normal operations • YELLOW = Call for assistance • RED = Line stopped
SELF-STOP (Jidoka)
Automatic detection and stopping when abnormality occurs. • Machine detects problem • Process stops automatically • Prevents defects from passing
Areas Affected (SQPC)
S
Safety
Immediate stop prevents injuries
Q
Quality
Defects caught at source
P
Productivity
Problems solved quickly
C
Cost
Reduces scrap and rework

## Slide 3
Self-Stop vs. Ordinary Automation
SELF-STOP (Jidoka)
✓ Reduces processes with simple circuits
✓ Self-stopping on abnormality detection
✓ Filters out defects at source
✓ Prevents equipment breakdowns
✓ Assists problem solving & prevention
✓ Clear indication of cause
✓ Enables root cause countermeasures
ORDINARY AUTOMATION
✗ Sophisticated equipment needing attention
✗ Stopped only by workers manually
✗ Passes on defects to next process
✗ Susceptible to breakdowns
✗ No indication for cause
✗ No prevention mechanism
✗ Problems hidden until too late
"Stop to fix problems" — short-term pain for long-term gain

## Slide 4
Andon Color Coding System
GREEN
Normal Operations
Production running within takt time, no issues
YELLOW
Call for Assistance
Operator needs help, line continues until fixed position
RED
Line Stopped
Emergency stop or unresolved issue, immediate attention required
Call Request Buttons
RED Button: Emergency Line Stop — Stops line immediately
YELLOW Button: Call for T/L — Line stops at end of cycle if not resolved

## Slide 5
Organization & Response Chain
Operator
Initiates the Call
Detects abnormality, pulls cord or pushes button
Team Leader
Answers the Call
Responds immediately, backs up operator, resets call
Group Leader
Supports & Tracks
Tracks downtime, reports to management, leads problem-solving
Response Standard
Team Leader must respond within takt time. If problem not resolved, line stops at fixed position.

## Slide 6
Call Board & Line Interlock
Call Board Functions
• Shows WHERE problem occurred (station #)
• Shows WHAT is stopped (process name)
• Displays call STATUS (active/cleared)
• Tracks DURATION of stoppage
• Visible from entire production area
• Audible alarm accompanies visual signal
Line Interlock Matrix
• Defines relationships between stations
• Upstream stop → downstream continues
• Prevents WIP buildup or starvation
• Configurable by process engineers
• Documented in interlock matrix
• Tested during line commissioning
Fixed Position Stop Principle
When YELLOW call is initiated, line continues to the next fixed position stop (end of cycle), giving Team Leader time to respond. If problem is resolved before reaching stop point, operator clears the call and line continues. If not resolved, line stops at fixed position — not mid-cycle.

## Slide 7
Implementation Benefits
Quality at Source
Defects caught immediately — no passing bad parts to next process
Reduced Scrap
Problems fixed before producing more defective units
Faster Problem Solving
Issues visible immediately, root cause identified while fresh
Team Empowerment
Operators authorized to stop line — ownership of quality
Data Collection
Every call tracked — downtime data drives improvement priorities
Culture Change
"Stop to fix" mentality replaces "keep running" mindset
Result: FTT improvement from 85% to 98%+ when properly implemented

## Slide 8
David E. Jones
TPS & Jidoka Implementation Expert
30 Years
Manufacturing Leadership
17 Years
Toyota Motor Corporation
$100M+
Documented Savings
Andon Systems | Jidoka Implementation | Quality at Source | Visual Management
Greater Nashville, TN | Business Proficient in Japanese | Japan Permanent Resident
dj@outcometn.com | (615) 689-1205 | outcome-usa.com