## Slide 1
EV Truck Assembly Line Design
Chassis & Cab Greenfield Concept
Product → Process → Equipment: A Toyota-Style Factory Planning Approach
David E. Jones
30 Years Manufacturing Leadership | 17 Years Toyota Motor Corporation

## Slide 2
Project Scope
$8M-$15M
CAPEX Range
9-12 mo
Timeline
11 HpV
Hours/Vehicle
70-80%
Confidence
Product
Electric Commercial Truck (Class 4-6) Complete vehicle assembly from frame to finished unit
Scope
• Chassis frame build-up & assembly
• Cab trim line (interior/exterior)
• Marriage station (cab-to-chassis)
• Final assembly & inspection
Deliverables
• 3D isometric concept layouts
• 2D AutoCAD floor plans
• Equipment specifications & suppliers
• CAPEX estimate with ranges
• Implementation timeline

## Slide 3
Line Configuration
CAB TRIM LINE
• Dual parallel conveyor system (LH/RH)
• 8-9m adjustable station pitch
• Parts kitting carts at each station
• Overhead cab delivery fixtures
• Andon visual management boards
CHASSIS LINE
• Frame ladder sequential build-up
• Axle & suspension sub-assembly
• Powertrain/battery integration
• Marriage station (precision cab drop)
• Final assembly, fluid fill, inspection
Process Flow
Frame Build
Axle S/A
Powertrain
Marriage
Final Assy
Inspection
Ship
Mixed-model capable — handles multiple truck variants on the same line

## Slide 4
Major Equipment & Suppliers
System
Description
Supplier
Purpose
Conveyors
AGV/Chain hybrid system
Dürr
Primary material flow
Cab Handling
Overhead hoist & fixtures
Demag/Kito
Ergonomic cab delivery
Marriage Station
Precision drop system
Custom Design
Cab-to-chassis alignment
Fastening
Torque-controlled tools
Atlas Copco
Critical joint assembly
Visual Mgmt
Andon boards
Vorne
Real-time OEE tracking
Material Handling
Kitting carts & AGVs
Creform/Toyota
Lean parts delivery
Equipment Selection Principle
Process requirements drive equipment decisions, not vendor proposals. Define the 'what' before engaging suppliers on the 'how'.

## Slide 5
Design Highlights
Mixed-Model Capable
Single line handles multiple truck variants — no changeover required
Scalable Design
Station pitch adjustable 7m to 9m based on volume requirements
Visual Management
Andon boards at every station — real-time performance visibility
Ergonomic Focus
Overhead handling systems eliminate manual lifting of heavy components
Automation Ready
Manual processes designed for future automation integration
Lean Material Flow
Kitting carts positioned for minimal operator walk time
Design philosophy: Start simple, prove the process, then automate

## Slide 6
Planning Methodology
Toyota-Style 5-Step Process
1
Product Analysis
Parts flow based on BOM structure — understand the product before designing the process
2
Takt Calculation
Line speed derived from customer demand × quality factors (FTT, AR, PR)
3
Process Design
Elemental time studies, human-machine separation, line balancing
4
Layout Development
3D visualization, aisle widths, material flow paths, ergonomic zones
5
Equipment Specification
Define requirements, select suppliers, develop CAPEX estimates
Each step builds on the previous — skipping steps creates rework and waste

## Slide 7
Relevant Experience
Toyota Motor Corporation
17 years
Lexus assembly plant launches — Fukuoka, Tahara, Toyota City. Final assembly planning, supplier development, TPS implementation.
Canoo Technologies
2 years
EV battery module & skateboard chassis assembly lines. $50M CAPEX managed. Scaled operations 10X.
Tubular Steel USA
3 years
Greenfield automotive plant launch. $0 to $8M revenue. 4% to 94% OEE.
Nissan North America
4 years
6M sq ft facility operations. 30K+ parts supply chain. $100M cost reduction.

## Slide 8
David E. Jones
Manufacturing Transformation & Factory Planning
30 Years
Manufacturing Leadership
17 Years
Toyota Motor Corporation
$100M+
Documented Savings
Greenfield Factory Design | TPS Implementation | Operational Turnarounds | EV/Battery Assembly
Greater Nashville, TN | Business Proficient in Japanese | Japan Permanent Resident
dj@outcometn.com | (615) 689-1205 | outcome-usa.com