## Slide 1
Product → Process → Equipment
A Toyota-Style Framework for Factory Planning
6-Step Methodology for Greenfield & Turnaround Manufacturing Operations
David E. Jones
17 Years Toyota Motor Corporation | Factory Launches in Japan, USA, Mexico

## Slide 2
The 6-Step Framework
Step 1
Product Parts Flow
Start with product structure
Step 2
Takt & Capacity
Calculate line speed from demand
Step 3
Process & Time
Elemental time studies
Step 4
Layout Design
Process → physical arrangement
Step 5
Logistics
Material flow & delivery
Step 6
4M Action List
Man, Material, Machine, Method
Each step builds on the previous — skipping steps creates rework and waste

## Slide 3
Step 2: Takt Time & Capacity Planning
Takt Time Calculation
Takt = Available Time / Customer Demand Gross Demand = Net ÷ (QR × AR × PR) • QR = Quality Rate (95% FTT) • AR = Availability Rate (98%) • PR = Performance Rate (90%)
Capacity Scenario Planning
• Single shift, standard hours
• Two shifts with overtime
• Three shifts, 6 days/week
• Maximum capacity (stress test)
Toyota Principle
Never design to theoretical demand. Factor in quality loss, equipment availability, and pace variation. A line designed for 100% utilization will fail at 85%.
This framework enables multi-site capacity balancing — allocating volume across plants based on capability, cost, and risk.

## Slide 4
Step 3: Elemental Time Study
Standard Time Elements (seconds)
Operation
Element
Time
Cab Install
Pick up part
10
BiQ yubi-sashi (check)
0.8
Set into position
5
Install/attach
20
BiQ yubi-sashi (verify)
0.8
Standard Time
36.6
TPS Quality Built-In (BiQ)
• Yubi-sashi: Point-and-call verification
• Every operation includes visual check
• Defects caught at source, not inspection
• Time budgeted into standard work
Human-Machine Separation
• VAW: Value-Added Work (human)
• NVAW: Non-Value-Added Work
• Machine cycle time (independent)
• Enables line balancing optimization

## Slide 5
Equipment Planning & CAPEX
Equipment Specification Framework
• Line-by-line equipment identification
• Process count drives conveyor/station qty
• Unique vs. general equipment classification
• Preferred supplier identification
• Unit cost × quantity = subtotal CAPEX
Sample Equipment Categories
• Conveyors (AGV, chain, stationary)
• Assembly fixtures & jigs
• Fastening tools (torque-controlled)
• Quality inspection equipment
• Material handling (lifts, hoists)
• Safety systems & guarding
Cost Control Principle
Equipment decisions flow from process requirements, not vendor proposals. Define the 'what' before engaging suppliers on the 'how'. This delivers 20-30% CAPEX savings.

## Slide 6
Step 6: 4M Problem Tracking (SQPC)
4M Classification
Man (人)
Skills, training, staffing
Material (料)
Parts, specifications, supply
Machine (机)
Equipment, tooling, maintenance
Method (法)
Process, standards, documentation
Priority Ranking (SQPC)
S - Safety
Always highest priority
Q - Quality
Customer-impacting issues
P - Productivity
Output, efficiency, cost
C - Cost
Budget, investment decisions
Execution Discipline
• Every issue logged with owner, target date, and 4M classification
• Daily/weekly review cadence with visible status (Open/Closed/Past Due)
• Escalation path for items requiring GM approval or funding

## Slide 7
Factory Planning Methodology
Proven across 30+ years of automotive manufacturing
Lexus Japan
3 plant launches
Canoo EV
$50M CAPEX managed
Tubular Steel
$0 → $8M greenfield
Gantri
700% output increase
David E. Jones | dj@outcometn.com | (615) 689-1205 | outcome-usa.com