## Slide 1
Mix-Model Production Systems
Equipment Design & Process Optimization for Flexibility
Enabling Heijunka Through Quick Change Fixtures & Human-Machine Separation
David E. Jones
30 Years Manufacturing Leadership | 17 Years Toyota Motor Corporation

## Slide 2
Two Essential Tools for Mix-Model
1. QUICK CHANGE FIXTURES
Equipment that enables mix-model sequence
• Single pallet handles multiple variants
• Zero changeover between models
• Automatic adaptation via recipe/AVI
• Cornerstone for leveled production
2. MAN/MACHINE CHARTS
Process optimization through separation
• Visualizes human vs machine actions
• Identifies waiting waste (both sides)
• Enables multi-machine operation
• Optimizes task order & walk paths
Why Use Together?
Quick change fixtures enable mix-model production at the equipment level. Man/machine charts optimize the operator's work within that mix-model environment. Together, they achieve true Heijunka — leveled production with minimal waste.

## Slide 3
Quick Change Fixture Types
Single Pallet Accommodates Multiple Product Variants
1. Flip Up/Down
Post Flip
Posts flip up or down to engage/disengage locators
2. Pin Flip
Pin Flip
Locating pins flip to different positions per model
3. Post Turn
Rotary
Posts rotate to present different locating surfaces
4. Post Slide
Linear
Posts slide laterally to accommodate width variation
5. Cantilever
Bolting
Work clamp positions via standardized hole patterns
Example Application:
5 powertrain variants on single pallet: • V6 3.5L Hybrid • V6 3.3L Gas • L4 2.4L Gas • L4 2.4L Hybrid • V6 3.5L 2GF
Key Principle: Zero changeover time between models = true sequence production

## Slide 4
Line Shape Selection
Form Follows Function — Design After Planning Steps 1 & 2
I / Y Shape
BEST for Mix-Model
Optimized for small component delivery along line, supports sequence & leveled production
U / C Shape
Good for Flex Volume
First/last operation by one person in low volume; NOT recommended for mix-model (difficult multi-product delivery)
F / L / J / K
Space Constrained
Used when facility doesn't allow straight 'I' shape
W Shape
Compact Alternative
Space efficient but requires extra material handling
⚠ Avoid "one team member – one machine syndrome" — separate human work from machine work

## Slide 5
Man/Machine Cycle Time Chart
Process Optimization Tool — One Page, One Chart
What the Chart Reveals
• Task order & sequence
• Man walk distances
• Man & machine return distances
• Machine positions & methods
• Job/task times
• Cycle rate change impacts
Chart Elements
X-Axis:
Time (seconds)
Y-Axis:
Distance (pitch/work zones)
Man Line:
Task start to end, walk paths
Machine Line:
Operation sequence & duration
Intersection:
Man × Machine sync points
Return:
Home position reset paths
Purpose
Enables process optimization by visualizing task order changes based on value stream and product structure. Identifies where man waits for machine (waste) and where machine waits for man (lost capacity).

## Slide 6
Human-Machine Separation Principle
The Problem: Waiting Waste
• Man waits for machine to complete cycle • Machine waits for man to load/unload • Both represent lost capacity • 'One man – one machine' locks in waste
The Solution: Separation
• Separate human work from machine work • Man initiates cycle, walks to next machine • Machine completes while man works elsewhere • One operator handles multiple machines
Man × Machine Must Match
Load Point
Man loads part → Machine clamps
Start Point
Man pushes button → Machine cycle begins
Unload Point
Machine completes → Man returns to unload
Result: 30-50% labor productivity improvement through multi-machine operation

## Slide 7
Implementation Results
Zero
Changeover Time
Between model variants
30-50%
Labor Productivity
Multi-machine operation
5+
Variants per Pallet
Single fixture handles all
100%
Sequence Capable
True Heijunka enabled
Where Applied
Magna Powertrain
5-variant engine assembly on single pallet system
Toyota Lexus Plants
Mixed-model final assembly lines (Fukuoka, Tahara)
Canoo Technologies
EV battery module assembly with multi-pack variants
Tubular Steel USA
High-speed tube forming with quick-change tooling

## Slide 8
David E. Jones
Mix-Model Production & Process Optimization Expert
30 Years
Manufacturing Leadership
17 Years
Toyota Motor Corporation
$100M+
Documented Savings
Quick Change Fixtures | Man/Machine Separation | Heijunka | Line Design | Kaizen
Greater Nashville, TN | Business Proficient in Japanese | Japan Permanent Resident
dj@outcometn.com | (615) 689-1205 | outcome-usa.com